## Slide 1
Computer Arithmetic

## Slide 2: Arithmetic & Logic Unit
Does the calculations
Everything else in the computer is there to service this unit
Handles integers
May handle floating point (real) numbers
May be separate FPU (maths co-processor)
May be on chip separate FPU (486DX +)

## Slide 3: ALU Inputs and Outputs

## Slide 4: Integer Representation
Only have 0 & 1 to represent everything
Positive numbers stored in binary
e.g. 41=00101001
No minus sign
No period
Sign-Magnitude
Two’s compliment

## Slide 5: Sign-Magnitude
Left most bit is sign bit
0 means positive
1 means negative
+18 = 00010010
 -18 = 10010010
Problems
Need to consider both sign and magnitude in arithmetic
Two representations of zero (+0 and -0)

## Slide 6: Two’s Compliment
+3 = 00000011
+2 = 00000010
+1 = 00000001
+0 = 00000000
 -1 = 11111111
 -2 = 11111110
 -3 = 11111101

## Slide 7: Benefits
One representation of zero
Arithmetic works easily (see later)
Negating is fairly easy
3 = 00000011
Boolean complement gives 11111100
Add 1 to LSB 11111101

## Slide 8: Geometric Depiction of Twos Complement Integers

## Slide 9: Negation Special Case 1
 0 = | 00000000
Bitwise not | 11111111
Add 1 to LSB | +1
Result | 1 00000000
Overflow is ignored, so:
- 0 = 0 

## Slide 10: Negation Special Case 2
-128 = | 10000000
bitwise not | 01111111
Add 1 to LSB | +1
Result | 10000000
So: | 
-(-128) = -128 X
Monitor MSB (sign bit)
It should change during negation

## Slide 11: Range of Numbers
8 bit 2s compliment
+127 = 01111111 = 27 -1
 -128 = 10000000 = -27
16 bit 2s compliment
+32767 = 011111111 11111111 = 215 - 1
 -32768 = 100000000 00000000 = -215

## Slide 12: Conversion Between Lengths
Positive number pack with leading zeros
+18 = 00010010
+18 = 00000000 00010010
Negative numbers pack with leading ones
-18 = 10010010
-18 = 11111111 10010010
i.e. pack with MSB (sign bit)

## Slide 13: Addition and Subtraction
Normal binary addition
Monitor sign bit for overflow
Take twos compliment of substahend and add to minuend
i.e. a - b = a + (-b)
So we only need addition and complement circuits

## Slide 14: Hardware for Addition and Subtraction

## Slide 15: Multiplication
Complex
Work out partial product for each digit
Take care with place value (column)
Add partial products

## Slide 16: Multiplication Example
 | 1011 | Multiplicand (11 dec)
 | 1101 | Multiplier (13 dec)
 | 1011 | Partial products
 | 0000 | Note: if multiplier bit is 1 copy
 | 1011 | multiplicand (place value)
 | 1011 | otherwise zero
 10001111 Product (143 dec)
 Note: need double length result

## Slide 17: Unsigned Binary Multiplication

## Slide 18: Execution of Example

## Slide 19: Flowchart for Unsigned Binary Multiplication

## Slide 20: Multiplying Negative Numbers
This does not work!
Solution 1
Convert to positive if required
Multiply as above
If signs were different, negate answer
Solution 2
Booth’s algorithm

## Slide 21: Booth’s Algorithm

## Slide 22: Example of Booth’s Algorithm

## Slide 23: Division
More complex than multiplication
Negative numbers are really bad!
Based on long division

## Slide 24: Division of Unsigned Binary Integers
001111
1011
100
1011 10010011
00001101
1011 001110
1011
Quotient
Dividend
Remainder
Partial Remainders
Divisor

## Slide 25: Division Algorithm
start
A = 0
M = Divisor Q = Dividend Count = n
Shift Left A,Q A = A - M
A<0
?
Q0 = 0
A = A + M
0
Q = 1
Count = Count - 1
Count = 0
?
Stop
Y
N
N
Y

## Slide 26: Example
A | Q | M = 0011
0000 | 0111 | Initial value
0000 | 1110 | Shift
1101 |  | Subtract
0000 | 1110 | Restore
0001 | 1100 | Shift
1110 |  | Subtract
0001 | 1100 | Restore
0011 | 1000 | Shift
0000 |  | Subtract
0000 | 1001 | Set Q0 = 1
0001 | 0010 | Shift
1110 |  | Subtract
0001 | 0010 | Restore

## Slide 27: Real Numbers
Numbers with fractions
Could be done in pure binary
1001.1010 = 24 + 20 +2-1 + 2-3 =9.625
Where is the binary point?
Fixed?
Very limited
Moving?
How do you show where it is?

## Slide 28: Floating Point
+/- .significand x 2exponent
Misnomer
Point is actually fixed between sign bit and body of mantissa
Exponent indicates place value (point position)
Sign bit
Biased Exponent
Significand or Mantissa

## Slide 29: Floating Point Examples

## Slide 30: Signs for Floating Point
Mantissa is stored in 2s compliment
Exponent is in excess or biased notation
e.g. Excess (bias) 128 means
8 bit exponent field
Pure value range 0-255
Subtract 128 to get correct value
Range -128 to +127

## Slide 31: Normalization
FP numbers are usually normalized
i.e. exponent is adjusted so that leading bit (MSB) of mantissa is 1
Since it is always 1 there is no need to store it
(c.f. Scientific notation where numbers are normalized to give a single digit before the decimal point
e.g. 3.123 x 103)

## Slide 32: FP Ranges
For a 32 bit number
8 bit exponent
+/- 2256  1.5 x 1077
Accuracy
The effect of changing lsb of mantissa
23 bit mantissa 2-23  1.2 x 10-7
About 6 decimal places

## Slide 33: Expressible Numbers

## Slide 34: IEEE 754
Standard for floating point storage
32 and 64 bit standards
8 and 11 bit exponent respectively
Extended formats (both mantissa and exponent) for intermediate results

## Slide 35: FP Arithmetic +/-
Check for zeros
Align significands (adjusting exponents)
Add or subtract significands
Normalize result

## Slide 36: FP Arithmetic x/
Check for zero
Add/subtract exponents
Multiply/divide significands (watch sign)
Normalize
Round
All intermediate results should be in double length storage

## Slide 37: Floating Point Multiplication

## Slide 38: Floating Point Division

## Slide 39: Required Reading
Stallings Chapter 8
IEEE 754 on IEEE Web site