## Slide 1
Instruction Sets: Addressing Modes and Formats

## Slide 2: Addressing Modes
Immediate
Direct
Indirect
Register
Register Indirect
Displacement (Indexed)
Stack

## Slide 3: Immediate Addressing
Operand is part of instruction
Operand = address field
e.g. ADD 5
Add 5 to contents of accumulator
5 is operand
No memory reference to fetch data
Fast
Limited range

## Slide 4: Immediate Addressing Diagram
Opcode
Instruction
Operand

## Slide 5: Direct Addressing
Address field contains address of operand
Effective address (EA) = address field (A)
e.g. ADD A
Add contents of cell A to accumulator
Look in memory at address A for operand
 Single memory reference to access data
No additional calculations to work out effective address
Limited address space

## Slide 6: Direct Addressing Diagram
Opcode
Instruction
Address A
Memory
Operand

## Slide 7: Indirect Addressing (1)
Memory cell pointed to by address field contains the address of (pointer to) the operand
EA = (A)
Look in A, find address (A) and look there for operand
 e.g. ADD (A)
Add contents of cell pointed to by contents of A to accumulator

## Slide 8: Indirect Addressing (2)
Large address space
2n where n = word length
May be nested, multilevel, cascaded
e.g. EA = (((A)))
Draw the diagram yourself
Multiple memory accesses to find operand
Hence slower

## Slide 9: Indirect Addressing Diagram
Opcode
Instruction
Address A
Operand
Memory
Pointer to operand

## Slide 10: Register Addressing (1)
Operand is held in register named in address filed
EA = R
Limited number of registers
Very small address field needed
Shorter instructions
Faster instruction fetch

## Slide 11: Register Addressing (2)
No memory access
Very fast execution
Very limited address space
Multiple registers helps performance
Requires good assembly programming or compiler writing
N.B. C programming
register int a;
c.f. Direct addressing

## Slide 12: Register Addressing Diagram
Opcode
Instruction Register Address R
Registers
Operand

## Slide 13: Register Indirect Addressing
C.f. indirect addressing
EA = (R)
Operand is in memory cell pointed to by contents of register R
Large address space (2n)
One fewer memory access than indirect addressing

## Slide 14: Register Indirect Addressing Diagram
Register Address R
Opcode
Instruction
Memory
Operand
Pointer to Operand
Registers

## Slide 15: Displacement Addressing
EA = A + (R)
Address field hold two values
A = base value
R = register that holds displacement
or vice versa

## Slide 16: Displacement Addressing Diagram
Opcode Register R
Instruction
Memory
Operand
Pointer to Operand
Registers
Address A
+

## Slide 17: Relative Addressing
A version of displacement addressing
R = Program counter, PC
EA = A + (PC)
i.e. get operand from A cells from current location pointed to by PC
c.f locality of reference & cache usage

## Slide 18: Base-Register Addressing
A holds displacement
R holds pointer to base address
R may be explicit or implicit
e.g. segment registers in 80x86

## Slide 19: Indexed Addressing
A = base
R = displacement
EA = A + R
Good for accessing arrays
EA = A + R
R++

## Slide 20: Combinations
Postindex
EA = (A) + (R)
Preindex
EA = (A+(R))
(Draw the diagrams)

## Slide 21: Stack Addressing
Operand is (implicitly) on top of stack
e.g.
ADD
Pop top two items from stack and add

## Slide 22: Instruction Formats
Layout of bits in an instruction
Includes opcode
Includes (implicit or explicit) operand(s)
Usually more than one instruction format in an instruction set

## Slide 23: Instruction Length
Affected by and affects:
Memory size
Memory organization
Bus structure
CPU complexity
CPU speed
Trade off between powerful instruction repertoire and saving space

## Slide 24: Allocation of Bits
Number of addressing modes
Number of operands
Register versus memory
Number of register sets
Address range
Address granularity

## Slide 25: Foreground Reading
Stallings chapter 10
Intel and PowerPC Web sites