## Slide 1
Memori External

## Slide 2: Jenis Memori External
Magnetic Disk
RAID
Removable
Optical
CD-ROM
CD-Writable (WORM)
CD-R/W
DVD
Magnetic Tape

## Slide 3: Magnetic Disk
Metal atau plastic dilapisi dg material yg bersifat magnet (iron oxide)
Jenis kemasan
Floppy
Winchester hard disk
Removable hard disk

## Slide 4: Format dan Organisasi Data
Lingkaran konsentris atau track
Ada Gap antar track
Gap sempit, kapasitas bertambah
Jumlah bit per track sama (kerapatan bervariasi)
Kecepatan putar tetap
Track dibagi menjadi beberapa sector
Ukuran minimum block adalah satu sector
Satu block bisa berisi lebih dari satu sector

## Slide 5: Fixed/Movable Head Disk
Fixed head
Ada satu head (r/w) per track
Head diletakkan pada tangkai yg tetap
Movable head
Hanya ada satu head per side
Diletakkan pada tangkai yg dpt bergerak

## Slide 6: Removable / Nonremovable
Removable disk
Dapat dilepas dari drive dan diganti dg disk lain
Memberikan kapasitas simpanan yg tak terbatas
Mudah melakukan transfer data antar sistem
Nonremovable disk
Terpasanang permanen dalam drive

## Slide 7: Winchester Hard Disk (1)
Dikembangkan oleh IBM di Winchester (USA)
Dikemas dalam satu unit
Berisi satu cakram atau lebih
Head sangat kecil
Handal

## Slide 8: Winchester Hard Disk (2)
Umum digunakan
Murah
Sbg external storage yg sangat cepat
Kapasitas semakin besar
Dalam orde GB

## Slide 9: Removable Hard Disk
ZIP
Murah
Banyak digunakan
100MB
JAZ
Mahal
1G
L-120 (a: drive)
Juga dpt untuk membaca 3.5” floppy

## Slide 10: Pencarian Sector
Harus dapat mengenali awal suatu track dan sector
Format disk
Menambahkan informasi tambahan
Memberi tanda awal track dan sector

## Slide 11: ST506 format (old!)
Gap1
Id Gap2 Data Gap3 Gap1
Id Gap2 Data Gap3
Track
Sync Byte
Head Sector CRC
Sync Byte
Data CRC

## Slide 12: Karakteristik
Fixed head atau movable head
Removable disk atau fixed disk
Single side atau double side
Single platter atau multiple platter
Mekanisme head
Contact (Floppy)
Fixed gap
Flying (Winchester)

## Slide 13: Multiple Platter
Satu head per side
Semua head di-join dan di-align
Track-track yg setiap platter membentuk cylinder
Data dipecah berdasarkan cylinder
Mengurangi gerakan head
Meningkatkan kecepatan (transfer rate)

## Slide 14: Kecepatan
Seek time
gerakan head ke track yg dituju
(Rotational) latency
Putar platter sampai posisi data dibawah head
Access time = Seek + Latency
Transfer rate

## Slide 15: RAID
Redundant Array of Independent Disks
Redundant Array of Inexpensive Disks
Ada 6 level
Tidak berhirarki
Sejumlah disks (fisik) yg dipandang sbg satu drive (logical) oleh Sistem Operasi
Data tersebar diantara disk fisik

## Slide 16: RAID 0
No redundancy
Data striped across all disks
Round Robin striping
Increase speed
Multiple data requests probably not on same disk
Disks seek in parallel
A set of data is likely to be striped across multiple disks

## Slide 17: RAID 1
Mirrored Disks
Data is striped across disks
2 copies of each stripe on separate disks
Read from either
Write to both
Recovery is simple
Swap faulty disk & re-mirror
No down time
Expensive

## Slide 18: RAID 2
Disks are synchronized
Very small stripes
Often single byte/word
Error correction calculated across corresponding bits on disks
Multiple parity disks store Hamming code error correction in corresponding positions
Lots of redundancy
Expensive
Not used

## Slide 19: RAID 3
Similar to RAID 2
Only one redundant disk, no matter how large the array
Simple parity bit for each set of corresponding bits
Data on failed drive can be reconstructed from surviving data and parity info
Very high transfer rates

## Slide 20: RAID 4
Each disk operates independently
Good for high I/O request rate
Large stripes
Bit by bit parity calculated across stripes on each disk
Parity stored on parity disk

## Slide 21: RAID 5
Like RAID 4
Parity striped across all disks
Round robin allocation for parity stripe
Avoids RAID 4 bottleneck at parity disk
Commonly used in network servers
N.B. DOES NOT MEAN 5 DISKS!!!!!

## Slide 22: Optical Storage CD-ROM
Originally for audio
650Mbytes giving over 70 minutes audio
Polycarbonate coated with highly reflective coat, usually aluminum
Data stored as pits
Read by reflecting laser
Constant packing density
Constant linear velocity

## Slide 23: CD-ROM Drive Speeds
Audio is single speed
Constant linier velocity
1.2 ms-1
Track (spiral) is 5.27km long
Gives 4391 seconds = 73.2 minutes
Other speeds are quoted as multiples
e.g. 24x
The quoted figure is the maximum the drive can achieve

## Slide 24: CD-ROM Format
00
00
FF
x 10
Min
Sec Sector Mode
Data
Layered ECC
12 byte Sync
4 byte Id
2048 byte 288 byte
2352 byte
Mode 0=blank data field
Mode 1=2048 byte data+error correction
Mode 2=2336 byte data

## Slide 25: Random Access on CD-ROM
Difficult
Move head to rough position
Set correct speed
Read address
Adjust to required location
(Yawn!)

## Slide 26: CD-ROM for & against
Large capacity (?)
Easy to mass produce
Removable
Robust
Expensive for small runs
Slow
Read only

## Slide 27: Other Optical Storage
CD-Writable
WORM
Now affordable
Compatible with CD-ROM drives
CD-RW
Erasable
Getting cheaper
Mostly CD-ROM drive compatible

## Slide 28: DVD - what’s in a name?
Digital Video Disk
Used to indicate a player for movies
Only plays video disks
Digital Versatile Disk
Used to indicate a computer drive
Will read computer disks and play video disks
Dogs Veritable Dinner
Officially - nothing!!!

## Slide 29: DVD - technology
Multi-layer
Very high capacity (4.7G per layer)
Full length movie on single disk
Using MPEG compression
Finally standardized (honest!)
Movies carry regional coding
Players only play correct region films
Can be “fixed”

## Slide 30: DVD - Writable
Loads of trouble with standards
First generation DVD drives may not read first generation DVD-W disks
First generation DVD drives may not read CD- RW disks
Wait for it to settle down before buying!

## Slide 31: Foreground Reading
Check out optical disk storage options
Check out Mini Disk

## Slide 32: Magnetic Tape
Serial access
Slow
Very cheap
Backup and archive

## Slide 33: Digital Audio Tape (DAT)
Uses rotating head (like video)
High capacity on small tape
4Gbyte uncompressed
8Gbyte compressed
Backup of PC/network servers

## Slide 34: Cloud Storage
Public Cloud
Cloud Aplikasi
Cloud Media Sosial
Cloud server vistual

## Slide 35: SEKIAN TERIMAKASIH
Disarikan dari berbagai Sumber :
http://ahyad.staff.gunadarma.ac.id/